## Slide 1: Farm Safety Basics for Youth
Supplies needed for tonight’s class:
Stop watch
Blank piece of paper
Basic art supplies
Farm Safety: (4:10) https://www.youtube.com/watch?v=rlLhnPcf1EA
Section 2

## Slide 2: Youth Fatality Facts
Every third day there is a death working in agriculture
48% of all fatal injuries from Agriculture
44.8 times more likely to be fatally injured in Agriculture

## Slide 3: Youth Injury Facts
Every day 33 youth are injured in Agriculture
Falls, animals, and off road vehicle use are 3 sources of injury
Hand, head, and leg injuries are most common
Livestock and dairy farms are top of the list, followed by crop farms

## Slide 4: Choose Safety!
Identify the hazards
Develop a plan to deal with the hazards
Consider consequences before action
Practice safe work habits
Wear PPE
Speak up for your own SAFETY!

## Slide 5: What is Risk?
Risk: “the chance you take of becoming injured by a hazard”
Risk is rated by it’s probability and consequences

## Slide 6: Risk Exposure / Severity
Example 1.
  Entering and exiting the skid steer under the boom?
    Frequent / Catastrophic
Example 2.
  Working with a new beef calf and mother?
    Occasional / Critical

## Slide 7: Instincts are Dangerous
Farm Safety with Animals: (4:18) https://www.youtube.com/watch?v=xh2-uwlWARA

## Slide 8: Where’s the Risk!
Courtesy of: www.bing.com

## Slide 9: Question Break
List a risky decision you have made?
What was the probability of injury due to exposure and severity of the decision?
How are you going to make a less risky decision next time?

## Slide 10: Reduce Risk
Recognize our own RISKY traits
Recognize when more training is needed
Remove hazards from the workplace
Use safety equipment CORRECTLY
Notes: 1. Are you a risk taker?
2. List the risk-taking situations you have experienced.
3. What is the exposure / severity of those risks? Chart: Section 2.2 page 4

## Slide 11: Reaction Time
“the time it takes for a person to react to an event or an emergency”
Factors affecting reaction time:
  Experience
  Age
  Fitness
  Fatigue
  Illness
  Pre-occupation
  Distraction
  Mood
  Weather
  Drugs/Medication
  Alcohol and Tobacco
  Machine Vibrations
  Poor Vision
  Poor Hearing

## Slide 12: Realistic Reaction Time
¾ of a second
  Slower than it takes for a tractor to reach the point of tipping over!
½ of a second
  A 540 PTO will turn 4.5 times before reaction can occur!
Notes: 1. Complete rpm question #4 on page 4 of 2.3.
2. How fast is your reaction time?
-use the stop watch on your phone to determine your reaction time!

## Slide 13: Age Appropriate Tasks
Age 12-13
  Hand raking/digging
  Limited power tool use with supervision
  Operating lawn mower or garden tractor
  Handling/assisting with animals
  Other low-risk tasks
Age 14-15
  Equipment Maintenance
  Manual feeding of livestock
  Operating non-articulated tractors for fieldwork
  Raking Hay
  Operating a pressure washer

## Slide 14: Age Appropriate Tasks
Age 16-18
  Ordinary use of tractors, self propelled machinery, augers, elevators, and other equipment
  Pulling oversize loads, simultaneous use of multiple vehicles, and applying chemicals (with proper training)
http://www.agdepartment.com/Images/LivestockPollution/tractor.jpg
Notes: 1. Can you think of specific jobs that you complete on the farm?
-Do they fit the age criteria suggested?

## Slide 15: Severe Weather
Areas of risk include:
  High Temperatures (heat cramps, heat exhaustion, heat stroke)
  High Humidity (thunderstorms, lightning, tornadoes)
  Winter Weather (Frostbite, Hypothermia, Slippery conditions)
Notes: 1. Know where to find the latest weather warnings!
2. Farming occurs everyday of the year…regardless of the weather!

## Slide 16: Heat and Cold Protection
Proper attire should be worn in heat and cold conditions
  Heat: Sunscreen, wide brim hat, bandana, long sleeve shirt, long trousers
  Cold: First layer T-shirt, second layer work shirt, third layer sweater, fourth layer jacket
Heat Index
Windchill
Notes: Further detail for protection is in the student manual!
How is Heat Illness prevented?
What is Hypothermia?

## Slide 17: Wind and Tornadoes
Check weather forecast
Observe threatening conditions
Remain alert to storms if a tornado “watch” is issued
Move to a safe shelter immediately if a tornado “warning” is issued
Go to basements or inner rooms of buildings away from windows
Do not try to outrun a tornado
Seek a low ditch for protection
Lie face down with hands over your head
Notes: 1. Watch for severe weather!

## Slide 18: Thunderstorms and Flooding
Lightning Risk- 30/30 Rule
Seek shelter away from water and “lightning rods”
Buildings, vehicles and cab tractors are a safe refuge
You can’t be sure what is under running water!
http://www.ipm.iastate.edu/ipm/icm/2004/3-22-2004/palle-seedinoculation.jpg
Notes: Topography that is low at risk of flooding and high topography is at risk of lightning!

## Slide 19: Housekeeping
Provide space for safe movement
Provide adequate lighting and ventilation
Install slip resistant flooring
Install covers on pits and floor openings
Always eliminate sharp edges
Always clearly mark exits
Always keep the farm clean and sanitary
Notes: There are many environmental hazards on a farm. Dust, Welding rays, Slippery floors
Proper Storage and Cleanup is important to keep the farm safe!

## Slide 20: Personal Dress
No jewelry or sandals!
Tie long hair back
Wear snug-fitting clothes
Wear leather shoes
Keep laces tied
Wear long pants
Wear a hat and gloves
Farm work isn’t a beauty pageant!
Photo courtesy of: www.bing.com
Notes: Working on the farm isn’t a beauty pageant!

## Slide 21: Hazard Signs
Read!
Respect!
Respond!

## Slide 22: Hand Signals
They are an important language!

## Slide 23: Personal Protective Equipment
Eye—goggles, face shield
Respiratory—dust/cartridge mask)
Head—caps, hard hats
Hearing—ear plugs, acoustic muff
Foot—steel toe shoe
Hand—Gloves
Notes: List 1 farm task which each area of PPE can keep you safe.

## Slide 24: First Aid and Rescue
Along with safe equipment, a safe work site should have:
  A person trained in CPR
  First Aid kit and supplies
  Emergency plan (with phone numbers)
  Location or site map for emergency responders
Notes: It’s really important! Let’s quickly read page 3 in section 2.11 together as a class.

## Slide 25: First Aid Equipment
Roller Bandages
Adhesive Tape
Sterile First-Aid Dressings and Compresses (various sizes)
Disinfectant Soap or Wound Cleaner
Tweezers
Scissors
Latex Gloves
Directions for Requesting Emergency Assistance

## Slide 26: Make a Farm Safety Poster
Themes to choose from:
1. Safety risks on the farm
2. Weather related farm safety
3. Safety choices for everyday
4. Farm safety languages
5. Response to a farm emergency
Modified Presentation- Marissa Morton SAAIP Top Jobs Intern

## Slide 27: Homework: Read Section 2 and complete the Section 2 worksheet
Tractor Safety Game
  Kahoot.it
Tractor Safety Game